## Slide 1: Recurrent Neural Networks (RNN) for Modeling of Nonlinear Systems
Sebastian Hirt | 19.01.2023
Lehrstuhl für Regelungstechnik

## Slide 2: Motivation
Problem:
  Complex System without analytic form
  Example: Pendulum with unknown friction model
Solution
  Train a model with measured data
  Prediction of future states with model

## Slide 3: Methods

## Slide 4: LSTM-Cell
Long-term dependency through cell state
Passing of new initial value to next timestep internally
Gates with trainable weights
activation function
Adapted from (Yu, Y., Si, X., Hu, C., & Zhang, J., 2019)

## Slide 5: Model
Example of model with 32 nodes and 2 hidden layers
Transfer of states to next time steps
Same weights at all time steps of individual Cells
Ability to predict indefinite future states
Fixed number of timesteps for training
t

## Slide 6: Dataset Creation

## Slide 7: Pendulum-Complex Dataset
Pushing a pendulum
Dampened due to friction
Varying shape of pushing force
200 different time series
Notes: q = c/m = 1
l = 1m, g = 9.81, m = 1, c = 1, f = 2
F(t) should be divided by ml, but nothing changes, bc both are 1.

## Slide 8: Drag-Complex Dataset
Pushing force on object
Drag on object
Varying of shape of pushing force
40 different time series
Notes: b = ½ * rho(density) * C_d(drag coefficient) * A(Area)

## Slide 9: Preparation for Training
Split into training, validation and test set
Scaling of data with MinMaxScaler to [-1,1] to match LSTM output
Transformation into correct format
  Initial condition given at first timestep, zero afterwards
  Force input given at every time step

## Slide 10: Putting it together
Calculation of loss from forward pass
Update of weights through backpropagation and Adam optimizer
Notes: For all batches of dataset:
  Add squared error over time steps (mean of different variables)
  Mean over batch
Then for multiple epochs

## Slide 11: Hyperparameter Search

## Slide 12: Manual Search
Monitoring validation loss for early stopping
Check hyperparameters one by one
Take best parameter for next step
Search order:
  Learning rate
  Number of layers
  Number of nodes in each layer
Training for 500 epochs, then 5000 with best model
Adapted from (Ryan, H. & Alexis C. 2022)
Loss
Underfitting
Overfitting
Epochs
Early stopping
Validation
Training
Notes: Could use automatic hyperparameter search as well
Training times on gtx 1060 3gb
  120 timeseries, 3000 timesteps, 500 epochs
    Five layer 30 min
    Two layer 15 min
    Nodes, lr not rly affecting time much
    two layers, 32 nodes, 5000 epochs ~2h
- inference times:
2 layer 64 nodes, 1000 length:
  0.035 s
  --> for one step: 0.000035 s (0.035ms, 35µs)
  fps (one step): 1/0.000035 = 28571.428571428572

## Slide 13: Hyperparameter Search - Learning rate and layers
Better training performance with higher learning rate and less layers
Validation loss
Validation loss

## Slide 14: Hyperparameter Search - Nodes
Higher training stability for smaller models and early stopping to save model with best validation loss
Validation loss
Notes: Larger models more difficult to train
Only training, not final performance, bigger models might get better later, have higher(lower) performance ceiling

## Slide 15: Evaluation and Conclusion

## Slide 16: Evaluation - Pendulum
Overall low error
Small error spikes on input change

## Slide 17: Evaluation - Drag
Rare large error
Error spikes on input change
Notes: No training sample too similar  not overfitted.
Error at input change sources:
  Maybe difficult to learn larger changes in hidden/cell states

## Slide 18: Conclusion and Future Work
Conclusion
  Training difficulties with larger models
  Error spikes on input change
  Clear ability to predict nonlinear dynamic system
  Recommendation:
    2 LSTM layers with 32/64 nodes and learning rate of 0.01 for similar systems
    New hyperparameter search for different/more complex systems
Future Work
  Deeper look into training instabilities with larger models necessary
  Testing for more complex ordinary differential equations
  Analysis on what and how much training data is necessary to achieve good results
Notes: Requirements for more complex systems:
  Stabilize training for larger models
  Size and type of datasets
  Further testing for specific situations
Create better dataset to test specific situations

## Slide 19
Thank You!

## Slide 20: References
Yu, Y., Si, X., Hu, C., & Zhang, J. (2019). A review of recurrent neural networks: LSTM cells and network architectures. Neural Computation, 31(7), 1235–1270.
Holbrook, R., &amp; Cook, A. (2022, May 5). Overfitting and underfitting. Kaggle. Retrieved January 12, 2023, from https://www.kaggle.com/code/ryanholbrook/overfitting-and-underfitting/tutorial

## Slide 21: Problem description
Pushing force:
Air resistance (Drag):
Simplification:
Resulting force:

## Slide 22: Problem description
Resulting force:
Express as second order differential equation:
Transform into system of two first order equations:
   use in odeint python function to get values of velocity and/or position